## Slide 1: Ch.5. Industrial Activities & Pollution
Past Activities Typically Conducted at Brownfields Sites | Typical Contaminants and Typical Sources
Agriculture | Volatile organic compounds (VOC); arsenic, copper, carbon tetrachloride, ethylene dibromide, and methylene chloride; pesticides; insecticides; herbicides; grain fumigants
Automotive refinishing and repair | Some metals and metal dust; various organic compounds; solvents; paint and paint sludges; scrap metal; waste oils
Battery recycling and disposal | Lead; cadmium; acids
Chloro-alkali manufacturing | Chlorine compounds; mercury
Coal gasification | Polynuclear aromatic hydrocarbons (PAH)
Cosmetics manufacturing | Heavy metals; dusts; solvents; acids
Dry cleaning activities | VOCs such as chloroform and tetrachloroethane; various solvents; spot removers; fluorocarbon 113
Electroplating operations | Various metals such as cadmium, chromium, cyanide, copper, and nickel
Glass manufacturing | Arsenic; lead
Herbicide manufacturing and use | Dioxin; metals; herbicides
Hospitals | Formaldehyde; radionuclides; photographic chemicals; solvents; mercury; ethylene oxide; chemotherapy chemicals
Incinerators | Dioxin; various municipal and industrial waste
Landfills—municipal and industrial | Metals; VOCs; polychlorinated biphenyl (PCB); ammonia; methane; household products and cleaners; pesticides; various wastes
Leather manufacturing | Toluene; benzene
Machine shops/metal fabrication | Metals; VOCs; dioxin; beryllium; degreasing agents; solvents; waste oils
Marine maintenance industry | Solvents; paints; cyanide; acids; VOC emissions; heavy metal sludges; degreasers
Munitions manufacturing | Lead; explosives; copper; antimony

## Slide 2
Paint/ink manufacturing | Metals (such as chromium, cadmium, lead, and zinc); VOCs; chloroform; ethyl benzene; solvents; paints; inks
Pesticide manufacturing | VOCs; arsenic; copper; pesticides; insecticides; herbicides; fungicides; xylene; chlorinated organic compounds; solvents
Petroleum refining and reuse | Petroleum hydrocarbons; benzene, toluene, ethylbenzene, xylene (BTEX); fuels; oil and grease
Pharmaceutical manufacturing | Lead; various organic chemicals; organic solvents
Photographic manufacturing and uses | Silver bromide; methylene chloride; solvents; photographic products
Plastics manufacturing | Polymers; phthalates; cadmium; solvents; resins; chemical additives; VOCs
Printing industry | Silver; solvents; acids; waste oils; inks and dyes; photographic chemicals
Railroad yards | Petroleum hydrocarbons; VOCs; BTEX; solvents; fuels; oil and grease; lead; PCBs
Research and educational institutions | Inorganic acids; organic solvents; metals and metal dust; photographic waste; waste oil; paint; heavy metals; pesticides
Scrap metal operations | Various metals (such as lead and nickel); PCBs; dioxin; transformers
Smelter operations | Metals (such as lead, copper, and arsenic)
Semiconductor manufacturing | Metals; VOCs; carbon tetrachloride; degreasing agents; solvents
Wood pulp and paper manufacturing | Chlorinated organic compounds; dioxin; furans; chloroform; resin acids
Wood preserving | Creosote; pentachlorophenol (PCP); arsenic; chromium; copper; PCB; PAHs; beryllium; dioxin; wood preservatives
http://www.ehso.com/contaminants.htm

## Slide 3
The textile industry is one of the largest polluters in the world. The World Bank estimates that almost 20% of global industrial water pollution comes from the treatment and dyeing of textiles.
http://www.sustainablecommunication.org/eco360/what-is-eco360s-causes/water-pollution
http://www.theguardian.com/environment/2013/jan/04/mps-compensate-heavy-industry-carbon
Pollution by heavy industries

## Slide 4
A worker cleaning dead fish at Guanqiao Lake in central China’s Hubei province last July. Hot weather and untreated industrial waste killed an estimated 50,000kg of fish. Drought, a growing population and booming industry led to critical water shortages. Last year the Yangtze river fell to its lowest level since 1866. Low water levels worsen the pollution diverted into lakes and rivers from manufacturing and sewage. guardian.co.uk
http://bis402environment.blogspot.kr/p/water-2.html